## Slide 1: Physically Unclonable Functions
Louis Barnes, Will Bourne, Ethan Harrison

## Slide 2: Hardware security
When most people think of security regarding electronic products, they might think of internet-based risks such as hacking or online scams. However, what is usually unconsidered is the security regarding their actual physical device.
A common problem with electronics, especially portable ones, is theft. Malicious parties usually steal a victim's electronic device so that they may access sensitive information. In some cases, criminals can even produce counterfeit hardware to imitate well-known brands. This problem can cost a lot of money and put people's privacy at risk.
The field of Electronics tasked with preventing this issue is called Hardware Security.
One helpful method of hardware security is the use of encryption. When a user stores sensitive information on a device, encryption will convert it to unreadable code without a cryptographic key to "unscramble" the data. People can use such keys also to verify that their device is an authentic product from a brand. The main challenge with encryption is producing a key that a malicious party cannot predict. With the technology available to criminals in the present day, the task can be tricky.
Notes: Briefly discuss the field of the hardware security and the problems it needs to tackle (give examples that lead to pufs)

## Slide 3: Physically unclonable functions
A highly reliable method of producing a cryptographic key is Physically Unclonable Functions (PUFs). PUFs utilise physical imperfections in a device's manufacturing to produce a key unique to that device. For the PUF to produce a key, a user sends an input signal or "challenge" to the device, and an output signal or "response" is received. Only trusted users would know the response signal, and that signal would be the needed key.
Furthermore, the device must be on for PUFs to produce a signal, and any physically invasive methods of acquiring information from the hardware alter the output response to a given challenge. As a result, PUFs make devices more physically secure.
Notes: Explain how PUFs work and how they help solve the problem of cyber security

## Slide 4: The bbc microbit v2
In the practical described by this presentation, we tested the SRAM of multiple BBC Microbit V2s for viability as a PUF. If a V2 Microbit is to be considered viable for use as a PUF, it must produce a repeatable response for a given input unique to other microbits of the same specification.
Insert microbit images
here
Insert Microbit spec here
Notes: Discuss the purpose of the practical and what the microbit was used for

## Slide 5: The hamming distance method
Note to self (Eef): cont writing here
Notes: Explain the hamming distance method and how it is calculated

## Slide 6: Acquiring data from the SRAM
Notes: Show how data was acquired from the SRAM and what data was required and why

## Slide 7: Analysis of Data
Notes: Briefly summarise the coding done to calculate hamming distance and carry out the appropriate statistics

## Slide 8: Results
Notes: Show figures from the report and discuss what can be inferred from them

## Slide 9: Conclusion
Notes: Argue as to whether a microbit is a viable device for creating PUFs